## Slide 1: Multiple vDPI Functions using DPDK and Hyperscan on OVS-DPDK Platform
Cheng-Chien SU
Fang-Chen KUO
LIONIC Corp.

## Slide 2: What is Deep Packets Inspection?
Packets flow
pass through the network
. . .
. . .
Content Inspection
. . .
Device Identification
Application Identification
Malicious Websites
Viruses
Hack’s
Intrusion
Router / Setup-Box Gateway

## Slide 3: Deep Packet Inspection Problem
Packet
Deep Packet Inspection
(Snort2.9.11)
1 Gbps (Line rate)
0.038 Gbps
reduced 96% throughput
Note: Intel Atom C3958 Platform

## Slide 4: Agenda
DPI Workflow
How to improvement DPI throughput in Intel Platform
  DPDK
  Hyperscan
  Content Merging
Multiple vDPI Function on OVS-DPDK Platform
Throughput Comparison

## Slide 5: DPI Workflow (1/2)
Packet In
Pre-Filter
Flow
Management
Flow
Action
Post-Checker
Packet Out
Network Interface Controller
Multiple Pattern Matching for Payload

## Slide 6: DPI Workflow (2/2)
Packet In
Pre-Filter
Flow
Management
Flow
Action
Post-Checker
Packet Out
Network Interface Controller
L3&L4 header matching
More exactly pattern matching

## Slide 7: DPI - Example
Packet In
Pre-Filter
Flow
Management
Flow
Action
Post-Checker
Packet Out
Network Interface Controller
alert tcp any any -> 192.168.0.0/16 any (msg:”VIRUS”; content:”virus”; dsize:300<>400; sid:10000;)
alert tcp any any -> 192.168.1.0/24 any (msg:”SKYPE”; content:”skype”; pcre:”/^skype=[0-9a-z]{10}/”; sid:20000;)
alert UDP 192.168.0.0/16 any -> any 53 (msg:”DNS Query”; content:”google”; pcre:”/\x01\x00.*google0x03.com/”; sid:30000;)

## Slide 8: How to improvement DPI throughput in Intel Platform
Packet In
Pre-Filter
Flow
Management
Flow
Action
Post-Checker
Packet Out
Network Interface Controller
Packet In
via DPDK
Packet Out
via DPDK
Pre-Filter
via Hyperscan

## Slide 9: Content Merging (1/2)
Pre-filter support regular expression
Increase the complexity of pattern to reduce the number of post check
Compatible with snort format

## Slide 10: Content Merging (2/2)
alert tcp $EXTERNAL_NET any -> $HOME_NET any (content:"|12 01|"; content:"|01 00 00 00|"; within:5; distance:2;)
Pattern: “\x01\x00\x00\x00”
Regular Expression: “\x12\x01.{2,3}\x01\x00\x00\x00”

## Slide 11: Lionic DPI SDK (1/2)
Lionic DPI-SDK provide antivirus, intrusion prevention system, application identification, device identification and web content filtering.
Lionic DPI-SDK is compatible with snort rule format.
Lionic DPI-SDK supports DPDK and Hyperscan.

## Slide 12: Lionic DPI SDK (2/2)
Hardware DPI – LA3000
Pattern Matching Processor (Silicon IP)
Software DPI
Pattern Matching Library
DPI Engine
Applications Services
Signature Database
Virus
Signature
Anti-Virus
IPS
Signature
Intrusion Prevention System
Application Signature
Application Identification
Web Content
Cloud Database
Web Content Filtering
Device Signature
Device Identification
Lionic DPI SDK

## Slide 13: Multiple vDPI Function on OVS-DPDK Platform
OvS-DPDK
DPDK vHost Acceleration
NIC
VM
vDPI Function
with Hyperscan
VirtIO
DPDK
VM
IPS
with Hyperscan
VirtIO
DPDK
VM
App Ident
with Hyperscan
VirtIO
DPDK
VM
Antivirus
with Hyperscan
VirtIO
DPDK
ovs-vswitchd
ofproto

## Slide 14: Test Platform Specification
Hardware – NEXCOM vDNA 1160
  Intel Atom C3958 SoC 16 cores @ 2GHz
  Memory: 32GB
  NIC: Intel i350 AM4 1GbE*4, Marvell PHY 1GbE*2
OS: Debian 9.4
OvS version: 2.9.0
DPDK version: 18.02.1
Hyperscan version: 4.7.0
Snort Version: 2.9.11
All the VMs are created by KVM and emulated by QEMU
Run IXIA IxLoad (version 3.30.58.17) on the provided environment

## Slide 15: Test Environment
OvS-DPDK
Guest VM
vDPI Function
with Hyperscan
VirtIO
DPDK
NIC
NIC
HTTP Traffic

## Slide 16: Throughput Comparison
vDPI Function | Throughput (Mbps) | Impact
No inter-VM | 872.29 | 0%
Snort (NFQ, Aho-Corasick) | 38.71 | 96%
Snort (NFQ, Hyperscan) | 95.84 | 89%
Snort (DPDK, Hyperscan) | 269.39 | 69%
Lionic-IPS (DPDK, Hyperscan) | 795.02 | 9%
Lionic-App_Ident (DPDK, Hyperscan) | 864.77 | 1%
Note: IPS rules are 9791, App_Ident rules are1858

## Slide 17: Snort Resource
Snort access packets via DAQ module
  Patch for DAQ-2.0.6 available at:
    http://seclists.org/snort/2016/q2/385
    Follows the instruction on the page to build Snort with patched DAQ module
Snort 2.9.x does not support using Hyperscan as MPSE
  Patch for Snort 2.9.8.2 are available at:
    https://01.org/zh/downloads/hyperscan-integration-snort-2.9.8.2-and-2.9.9.0?langredirect=1
  Some modification based on the patch to support Snort 2.9.11.1

## Slide 18: THANK YOU!
arthur.su@lionic.com
kuo.kuo@lionic.com